## Slide 2
Photonics and
AA station design
Peter Maat – ASTRON

## Slide 3
Analog Optical Link Technology in the SKA
  AA-low Antenna Element Connection
  AA-mid Tile Connection
  Wideband SPF Connection
  PAF Antenna Element Connection
RFoF Technology for the SKA
General design of RFoF link
Why Photonic Technology?
  Broadband / High Frequency
  Immunity for RFI
  Galvanic Isolation
  Lightning Resistant
  Light Weight
  Small Space Envelope

## Slide 4
Current Technology
RFoF Technology for the SKA
Syntonics
Finisar
Use PCB based RFoF technology
Expensive
Large size/volume
No easy integration

## Slide 5
Components
Lasers
  Fabry-Perot DFB / DBR VCSEL
Issues
  Availability in all l windows
  Modulation bandwidth
  Output power
  Temperature control

## Slide 6
Modulators
  Mach-Zehnder interferometer modulator
  Electro-absorption modulator
Detectors
  PIN
  APD
Issues
  Availability at all l’s
  Modulation bandwidth
  Input power
Components

## Slide 7
RFoF Technology for the SKA
Issues:
  External Modulation vs. Direct Modulation
    EM: more expensive
    EM: better link gain
    Equal SFDR and transmission distance
  Single mode vs. multimode
    Low cost
    Dispersion Issues
  Transmission distance limitations
    Available optical power
    Chromatic dispersion
      Carrier suppression effect
      FP laser: distance: 2 km @ 1 GHz
    Modal dispersion
    Fiber related distortions

## Slide 8
Photonic Coax
RFoF Technology for the SKA

## Slide 9
Direct modulated DFB
  Detector: responsivity ~ 0.9 A/W
  Laser: slope efficiency ~ 0.05 – 0.3 W/A
  Link gain ~ -25 dB
Cost Level: ~ 100 €
RFoF Technology for the SKA

## Slide 10
RF systems with direct modulation AOL
PmaxRFin = -50 dBm
PmaxRFout = 0 dBm
150 dB/Hz
160 dB/Hz
170 dB/Hz
NF < 6 dB requirement is satisfied for:
  Pop > -8 dBm
  RIN = -150 dB/Hz
  Bandwidth of 1.2 GHz
RFoF Technology for the SKA

## Slide 11
PmaxRFin = -50 dBm
PmaxRFout = 0 dBm
150 dB/Hz
160 dB/Hz
170 dB/Hz
For 200 MHz – 1.4 GHz: SFDR = 41.5 dB
For 70 MHz – 240 MHz: SFDR = 50 dB (1)
For Dn = 3 GHz: SFDR = 37.5 dB
Dynamic range is limited by antenna and LNA noise
RF systems with direct modulation AOL
RFoF Technology for the SKA

## Slide 12
Cost and Power
DM AOL system cost: 255 Euro / Power: 0.62 W
Now: ~100 Euro

## Slide 13
Optical Tx/Rx Technology: next step
High cost level caused by expensive packaging
Technology development for cost reduction
  Multiple components in a module: component integration
  Lower cost packaging technology
Follow the market trends to obtain low cost technology
Connect with industry to have the technology available in time
Market trend: parallel Tx/Rx technology for e.g. 100GbE
Market trend: low cost optical interconnect technology for data centers

## Slide 14
Example 1: IBM
Example 2: TE Connectivity
Optical Tx/Rx Technology: next step

## Slide 15
Future work
Inventory low cost DFB, FP, VCSEL technology
Investigation of Tx and Rx phase and amplitude stability in climate chamber (/field test)
Development of PCB based low power / low cost TX/RX technology

## Slide 17
Noise sources:
    Thermal noise
    Shot noise
    RIN
Direct Modulation: Tx/Rx Noise
RFoF Technology for the SKA

## Slide 18
Direct Modulation: Tx/Rx Distortion
NF = ~32 dB
IIP2 = 52 dBm
IIP3 = 33 dBm
OIP3 = 6 dBm
OIP2 = 25 dBm
IMF2 = 47 dB (1 GHz)
IMF3 = 49 dB (1 GHz)
RFoF Technology for the SKA