## Slide 1: A New Antenna Calibration algorithm for AA single station snapshot correlation S.Salvini, F.Dulwich, B.Mort, K.Zarb-Adami stef.salvini@oerc.ox.ac.uk

## Slide 2: Content
Fundamentals
Results 1: Chilbolton LOFAR
Results 2: Simulated sky tests (experiments)

## Slide 3: Content
Fundamentals
Results 1: Chilbolton LOFAR
Results 2: Simulated sky tests (experiments)

## Slide 4: Algorithm motivation
Antenna calibration for gains and phases
Antenna cross-correlation matrix available
Scalable to
  LOFAR station (~100 antennas)
  LOFAR core (~300 antennas)
  SKA Phase 1 AA (~1,000 antennas)
Model sky availability

## Slide 5: Algorithm Requirement
If N is the number of antennas ...
Speed and scalability with N
O(N2) floating-point operations throughout
Automatic
  “Tuning” parameters available – defaults usually sufficient
L2 (least-squares) minimisation
  Distance between model sky and calibrated observation
Accuracy and Robustness
  In particular wrt incomplete visibilities
    Missing baselines
    Partial cross-correlation
Limited dependency on the model sky complexity
  The main body of the algorithm does not depend on the model sky

## Slide 6: Some Linear Algebra
Invariants
  What is preserved under a transformation
  The algorithm is based on that
The SVD
  Unique decomposition
  U, V are unitary matrices, Σ is a diagonal matrix
    U ∙ UH = UH ∙ U = I; V ∙ VH = VH ∙ V = I;
    σi = Σi,i ≥ 0 is the i-th largest singular value
  Singular values are invariant under right or left application of any unitary matrix
    σ (A) = σ (W ∙ A ∙ Y) for any A, W, (W, Y unitary)
    Also ║ A ║2 = ║ W ∙ A ∙ Y ║2
A = UH ∙ Σ ∙ V

## Slide 7: Image and Visibility
Visibilities V  image I by 2-D Fourier Transform or similar
Fourier transforms are unitary
  F-1 = FH
Hence
  V = FH ∙ I∙ FH
  the singular values are preserved: σ (I) = σ (F ∙ V ∙ F) = σ (V)
  Iterating over the singular space of V is “equivalent” to iterating over the singular space of I (F is known)
I is real hence V is Hermitian: V = VH
For Hermitian matrices, eigenvalues are real and equal to the singular values σi apart the sign (±).
  I = F ∙ V∙ F

## Slide 8: The Algorithm
Initialisation (V are the observed visibilities)
For each pass
  Repeat until convergence
    Set the missing elements of V
    Get the largest eigenvalues and eigenvectors of V (the number of eigenvalues is adjusted dynamically)
    Compute the new correction to V using the largest eigenvalues
    Check for convergence
  Purge the negative eigenvalues if required
  Carry out a first preliminary calibration
Compute the complex gains
  If only one eigenvalue is required  immediate complex gains are obtained
  If more than one eigenvalue is required (rank-k problem k > 1)
    New algorithm, much faster than Levenberg-Marquardt or line search

## Slide 9: Algorithm components
Largest eigenvalues computation – both O(N2)
  Lanczos with complete reorthogonalisation
  Power (subspace) iteration with Raileigh-Ritz estimates
L2 minimisation
  Levenberg-Marquardt far too slow
  New algorithm is O(N2)
    Iterative one-sided solution
    Attempts to “jump” between convergence curves
    Very fast convergence
    It appears to work also for “brute force” approach, i.e. Minimise distance between observed and model visibilities (although with larger errors)

## Slide 10: Some further considerations
From the measurement equation
Where
  Complex gain Γ is diagonal
Hence
  Error of phases only, unitary transformation: easy problem
  Error of gains: difficult problem – it “scrambles” the eigenvalues

## Slide 11: Content
Fundamentals
Results 1: Chilbolton LOFAR
Results 2: Simulated sky tests (experiments)

## Slide 12: Chilbolton LBA LOFAR Station
Chilbolton LBA LOFAR station data
  Thanks to Griffin Foster!
Channel 300: 58.4 MHz
  Other channels also available
  Sequence of snapshots
  Observations spaced by ~520 seconds
Model sky of increasing complexity
  2 sources
  500 sources
  5,000 sources

## Slide 13: Model Sky
2 sources
5000 sources
500 sources

## Slide 14: 58.4 MHz – 500 sources model sky

## Slide 15: Timing and performance

## Slide 16: Antenna Gains

## Slide 17: Content
Fundamentals
Results 1: Chilbolton LOFAR
Results 2: Simulated sky tests (experiments)

## Slide 18: Simulated Sky
Antennas
  STD of gains errors ~ 50%
  STD of phase errors: ~ 2 π rad
Noise:
  equivalent to 150 K
    Diagonal elements of noise:
    Off-diagonal elements of noise: G is Gaussian random variate, with M the number of integration points
Number of integration points M = 1,000,000
  Corresponding to sampling rate 1 GHz, channelised into 1,000 channels, integrated for 1 second

## Slide 19: Some performance figures
Simulated sky
MATLAB code
My own laptop (Intel Core 2 i7, 2.5 GHz, Windows)
No. Antennas | Equivalent to | Time (seconds)
96 | LOFAR station | 0.06
351 | > LOFAR core | 0.12
1,000 | SKA Phase 1 ? | 0.88

## Slide 20: 96 Antennas Simulation

## Slide 21: 351 Antennas Simulation

## Slide 22: 1,000 Antennas Simulation

## Slide 23: One or more eigenvalues?
Near degeneracy between eigenvalues causes havoc!
  No longer individual eigenvalues
  The whole near degenerate subspace
Rank 1 can optimise trivially
For rank k, k > 1 no simple solution
  Full L2 minimisation
  Simple algorithm works well
    0.5 seconds using LM
    ~ 0.02 secs using the new alg
Chilbolton LOFAR LBA
  2 to 4 eigenvalues
Code chooses automatically

## Slide 24: Realistic simulated sky – 351 antennas
Simulated sky
  > 24,000 sources
  Same corruptions as before
  Same noise as before
20 calibration sources
2 eigenvalues used

## Slide 25: Missing Baselines (351 antennas case)
What if baselines (i.e. Antenna pairs) are removed from V?
  Partial cross-correlation (too many antennas)
  Missing data
  Removal of short baselines
Computation using “brute force” approach (less accurate)
Missing baselines
0 %
25%
50 %
75 %
90 %
95 %
98 %

## Slide 26: Conclusions
Fast
  Number of operation is O(N2)
  Prototype code in MATLAB
    Expected some gains in performance when ported to a compiled language (C, C++, Fortran)
  Even if it fails, worth using it first: computationally cheap
  Starting point for much more complex optimisations
Robust
Extra work always needed, but promising
  Any suggestions?

## Slide 27
Thank you for your attention!
Any questions?
Comments and suggestions would be very helpful