## Slide 1
Prof. Steven Tingay (ICRAR, Curtin University), MWA Director
December 2011: Taking the AA Programme into SKA Pre-construction
ASTRON, December 12 - 16, 2011
The Murchison Widefield Array
and SKA AA developments
MWA configuration

## Slide 2: The Murchison Widefield Array
One of three SKA Precursor instruments: Pathfinder on an SKA candidate site. The only low frequency SKA Precursor.
Analog beamformer
“Tile”
8 Tiles per receiver
Receiver
Correlation
Data archive/processing
80 – 300 MHz;
30 MHz of instantaneous bandwidth;
40 kHz channels, 0.5 second integrations;
3 km maximum baseline;
128 tiles.
Fine PFB
Epoch of Reionisation; Solar Physics; Continuum surveys; Transients

## Slide 3
Perth

## Slide 4
300 m
300 m

## Slide 5
Ben McKinley
Divya Oberoi/
Lynn Matthews
Chris Williams

## Slide 6: MWA enters the final construction phase
  Build-out to 512 antennas not possible, due to NSF funding decision;
  MWA de-scoped to 128 tiles;
  Readiness reviews (engineering/science) completed in November 2011;
  Fully funded project in Australia (remaining construction cost ~$8m)
3 km
100 m
Receivers
Tiles

## Slide 7
  Construction and supply contracts executed.
  Infrastructure (trenches, power and fibre reticulation): enough for 256 antennas;
  128 Tiles and beamformers (supplied by Burns Industries, NH;
  16 receivers (supplied by SME, Poseidon Scientific Instruments, Fremantle);
  GPU-based correlator (supplied by IBM);

## Slide 8
  CSIRO infrastructure.
  160 dB shielded building;
  10 Gbps connection to Perth;
  15 PB data storage @ $80m Pawsey supercomputing centre
10 Gbps for MWA

## Slide 9: MWA and SKA AA development
MWA has infrastructure capacity built for 256 tiles, but will
only deploy 128 tiles in the first instance. Excess infrastructure.
300 m diameter areas close to power and fibre connections

## Slide 10: A proposition to the AA team
Excess MWA infrastructure could host AA instrumentation during SKA pre-construction:
At least 2 x 300 m diameter areas for AA antennas;
9 x concrete pads to accommodate receivers/beamformers etc;
Power (240 V AC, 10 A outlets). Approximately 3 kV total excess over 9 pad locations;
~200 fibres excess over 9 pad locations, connected to 10 water cooled racks in central 160 dB shielded building;
10 Gbps connection from shielded building to Pawsey Centre in Perth. Approximately 2 – 3 Gbps excess on this link;
15 PB storage facility at Pawsey (plus massive compute – CPU/GPU).

## Slide 11
Advantages for AA development:
Full signal path from field to archive;
Quick and inexpensive start for AA testing at radio quiet location;
Saves infrastructure development costs (approvals, agreements, contractors, management etc);
Infrastructure is already RFI qualified;
Cross-correlation of AA antennas with MWA antennas for testing?;
Help from MWA team: Dr Randall Wayth (MWA Commissioning Scientist)

## Slide 12: Summary
MWA prototype phase complete: science results being published.
Final MWA construction phase commenced:
  Construction complete by November 2012;
  Commissioning underway by July 2011;
  First calls for science proposals in first half 2013.
Excess MWA infrastructure (full signal path from field to archive) could help AA development program get off to a flying start in SKA pre-construction phase.