## Slide 1: VLBI Techniques
VLBI Arrays: a brief tour
Model / delay constituents
Getting the most out of VLBI phases
  Observing tactics / propagation mitigation
Wide-field mapping
Concepts for the VLBI Tutorial
Bob Campbell, JIVE
ERIS #7, Dwingeloo . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . (18 oct 2017)
RadioNet has received funding from the European Commission’s Horizon 2020 Research and Innovation Programme under grant agreement No, 730562.

## Slide 2
T
h
e
E
V
N

## Slide 3: The EVN (European VLBI Network)
Composed of existing antennas
  generally larger (32m – 100m): more sensitive
  baselines up to 10k km (8k km from Ef to Shanghai, S.Africa)
  down to 17 km (with Jb-Da baseline from eMERLIN)
  heterogeneous, generally slower slewing
Frequency coverage [GHz]:
  workhorses: 1.4/1.6, 5, 6.0/6.7, 2.3/8.4, 22
  niches: 0.329, UHF (~0.6-1.1), 43
  frequency coverage/agility not universal across all stations
Real-time e-VLBI experiments
Observing sessions
  Three ~3-week sessions per year
  ~10 scheduled e-VLBI days per year
  Target of Opportunity observations

## Slide 4: EVN Links
Main EVN web page: www.evlbi.org
  EVN Users’ Guide: Proposing, Scheduling, Analysis, Status Table
  EVN Archive
Proposals: due 1 Feb., 1 June, 1 Oct. (23:59:59 UTC)
  via NorthStar web-tool: proposal.jive.eu
User Support via JIVE (Joint Institute for VLBI ERIC)
  www.jive.eu
  RadioNet trans-national access
Links to proceedings of the biennial EVN Symposia:
  www.evlbi.org/meetings
  History of the EVN in Porcas, 2010, EVN Symposium #10

## Slide 5: Real-time e-VLBI with the EVN
Data transmitted from stations to correlator over fiber
Correlation proceeds in real-time
  Improved possibilities for feedback to stations during obs.
  Much faster turn-around time from observations  FITS;
  permits EVN results to inform other observations
  Denser time-sampling (beyond the 3 sessions per year)
  EVN antenna availability at arbitrary epochs remains a limitation
Disk-recorded vs. e-VLBI: different vulnerabilities
  Recorded e- and/or e-shipping approaching best of both worlds

## Slide 6: The VLBA (Very Long Baseline Array)
Globals: EVN + VLBA (+ GBT + JVLA)
  proposed at EVN proposal deadlines (1Feb, 1Jun, 1Oct)
  VLBA-only proposals: 1Feb, 1Aug
VLBA URL: science.lbo.us
Homogeneous array (10x 25m)
  planned locations, dedicated array
  Bslns ~8600–250 km (~50 w/ JVLA)
  faster slewing
  HSA (+ Ef + Ar + GBT + JVLA)
Frequency agile
  down to 0.329, up to 86 GHz
Extremely large proposals
  Up towards 1000 hr per year

## Slide 7: East Asian VLBI Networks
Chinese (CVN): 4 ants., primarily satellite tracking
Korean (KVN): 3 ants., simultaneous 22, 43, 86, 129 GHz
VERA: 4 dual-beam ants., maser astrometry 22-49 GHz
  KaVA == KVN + VERA (issues separate KaVA calls for proposals)
Japanese: various astronomical & geodetic stations

## Slide 8: Other Astronomical VLBI Arrays
Global mm VLBI Network (GMVA)
  Effelsberg, Onsala, Metsahövi, Pico Veleta, NOEMA, KVN, most VLBAs, Green Bank (LMT, ALMA)
86 GHz
~2 weeks of observing per year
Coordinated from MPIfR Bonn
Long Baseline Array
  Only fully southern hemisphere array
Can now propose joint EVN+LBA obs
  growing number of east-Asian EVN stations provide lots of N-S baselines
  LBA—western EVN ~12k km (< 1 hr)

## Slide 9: IVS (International VLBI Service)
VGOS: wide-band geodetic system (4x 2GHz over 2-14 GHz)
IVS web page: ivscc.gsfc.nasa.gov
  Mirror: ivscc.bkg.bund.de
History of geodetic VLBI (pre-IVS):
  Ryan & Ma 1998, Phys. Chem. Earth, 23, 1041
VLBI as space geodesy
  cf: GPS, SLR/LLR, Doris
Frequency: 2.3 & 8-9
some at 8-9 & 27-34
Geodetic VLBI tactics:
  many short scans
  fast slews
  uniform distribution of stations over globe

## Slide 10: Some rule-of-thumb VLBI scales
Representative angular scales: 0.1 — 100 mas
Physical scales of interest:
  Angular-diameter distance DA(z)
  Proper-motion distance DM(z)  μ to βapp conversion
  DA turns over with z (max z~1.6), DM doesn’t
Brief table, using Planck 2015 cosmology parameters (from J.P. Rachen colloquium, Dwingeloo 11jun2015)
z | 1 mas subtends (DA) | βapp for 0.1 mas/yr (DM)
0.1 | 1.8 pc | 0.66 c
0.5 | 6.4 pc | 3.1 c
1 | 8.3 pc | 5.4 c
1.6 | 8.4 pc | 7.4 c
3 | 8.0 pc | 10.3 c

## Slide 11: VLBI vs. shorter-BI
Sparser u-v coverage
More stringent requirements on correlator model to avoid de-correlating during coherent averaging
No truly point-like primary flux calibrators in sky
Independent clocks & equipment at the various stations

## Slide 12: VLBI a priori Model Constituents

## Slide 13: VLBI a priori Model: References
IERS Tech.Note #36, 2010: IERS Conventions 2010
  www.iers.org link via Publications // Technical Notes
Urban & Seidelmann (Eds.) 2013, Explanatory Supplement to the Astronomical Almanac (3rd Ed.)
IAU Division A (Fundamental Astronomy; was Div.I)
  www.iau.org/science/scientific_bodies/divisions/A/info
SOFA (software): www.iausofa.org
Global Geophysical Fluids center: geophy.uni.lu
Older (pre- IAU 2000 resolutions):
  Explanatory Supplement to the Astronomical Almanac 1992
  Seidelmann & Fukushima 1992, A&A, 265, 833 (time-scales)
  Sovers, Fanselow, Jacobs 1998, Rev Mod Phys, 70, 1393

## Slide 14: VLBI Delay (Phase) Constituents
Conceptual components:
  τobs = τgeom + τstr + τtrop + τiono + τinstr + εnoise
Instrumental Effects
Source Structure
Source/Station/Earth orientation
τgeom = -[cosδ {bx cos H(t) – by sin H(t)} + bz sinδ] / c
where: H(t) = GAST – R.A.
and of course: φ = 2πωτp
Propagation
for φobs: ± N lobes

## Slide 15: Closure Phase
However, φstr is baseline-based: it does not cancel
  Closure phase can be used to constrain source structure
  Point source  closure phase = 0
  Global fringe-fitting / Elliptical-Gaussian modelling
Original ref: Rogers et al. 1974, ApJ, 193, 293
φcls = φAB + φBC + φCA
Independent of station-based Δφ
  propagation
  instrumental
But loses absolute position info
  degenerate to an arbitrary Δφgeom added to a given station
A
C
B

## Slide 16: Difference Phase
Differential astrometry on sub-mas scales:
 Phase Referencing 
Another differential φ measure
  pairs of sources from a given bsln
(Near) cancellations:
  propagation (time & angle between sources)
  instrumental (time between scans)
There remains differential:
  δφstr (ideally, reference source is point-like)
  δφgeom (contains the position offset between the reference and target)
Ref.
Targ.

## Slide 17: Phase-Referencing Tactics
Extragalactic reference source(s) (i.e., tied to ICRF2)
  Target referenced to an inertial frame
Close reference source(s)
  Tends towards needing to use fainter ref-sources
Shorter cycle times between/among the sources
  Shorter slews (close ref-sources, smaller antennas)
  Shorter scans (bright ref-sources, big antennas)
High SNR (longer scans, brighter ref-sources, bigger antennas)
Ref.src structure (best=none; if not, then not a function of ν or t)
In-beam reference source(s) – no need to “nod” antennas
  Best astrometry (e.g., Bailes et al. 1990, Nature, 319, 733)
  Requires a population of (candidate) ref-sources
  VERA multi-beam technique / Sites with twin telescopes

## Slide 18: Where to Get Phs-Ref Sources
RFC Calibrator search tool (L. Petrov)
VLBA Calibrator search tool
  Links to both via www.evlbi.org
    under: VLBI links // VLBI Surveys, Sources, & Calibrators
  List of reference sources close to specified position
  FD (2 bands) on short & long |B|; Images, Amp(|u-v |)
Multiple reference sources per target
  Estimate gradients in “phase-correction field”
  AIPS memo #111 (task ATMCA)
Finding your own reference sources (e-EVN obs)
  Sensitive wide-field mapping around your target
  Go deeper than “parent” surveys (e.g., FIRST, NVSS)
Notes: 18

## Slide 19: Celestial Reference Frame
Reference System vs. Reference Frame
  RS: concepts/procedures to determine coordinates from obs
  RF: coordinates of sources in catalog; triad of defining axes
Pre-1997: FK5
  “Dynamic” definition: moving ecliptic & equinox
  Rotational terms / accelerations in equations of motions
ICRS: kinematic  axes fixed wrt extra-galactic sources
  Independent of solar-system dynamics (incl. precession/nutation)
ICRF2: most recent realization of the ICRS
  IERS Tech.Note #35, 2009: 2nd Realization of ICRF by VLBI
  295 defining sources (axes constraint); 3414 sources overall
  Median σpos~ 100-175 μas (floor ~40 μas); axis stability ~10 μas
  More emphasis put on source stability & structure
Process to create ICRF3 underway

## Slide 20: Faint-Source Mapping
Phase-referencing to establish Dly, Rt, Phs corrections at positions/scan-times of targets too faint to self-cal
Increasing coherent integration time to whole observation
  Beasley & Conway 1995, VLBI and the VLBA, Ch 17, p.327
  Alef 1989, VLBI Techniques & Applications, p.261

## Slide 21: Differential Astrometry
Motion of target with respect to a reference source
  Extragalactic ref.src.  tied to inertial space (FK5 vs. ICRF)
  Shapiro et al. 1979, AJ, 84, 1459 (3C345 & NRAO 512: ’71-’74)
Masers in SFR as tracers of Galactic arms
  BeSSeL: bessel.vlbi-astrometry.org
Pulsar astrometry (birthplaces, frame ties, ne)
  PSRPI: safe.nrao.edu/vlba/psrpi
Stellar systems: magnetically active binaries, exo-planets
PPN γ parameter: Lambert et al. 2009, A&A, 499, 331
Frame dragging (GP-B): Lebach et al. 2012, ApJS, 201, 4
IAU Symp #248: From mas to μas Astrometry

## Slide 22: Phs-Ref Limitations: Troposphere
Station ΔZD  elevation-dependent Δφ
  Dry ZD ~ 7.5ns (~37.5 cycles of phase at C-band)
  Wet ZD ~ 0.3ns (0.1—1ns) but high spatial/temporal variability
Water-vapor radiometers to measure precipitable water along the antenna’s pointing direction
ZD
ZD x mapping function
ΔZD
ΔZD x m.f.

## Slide 23: Troposphere Mitigation
Computing “own” tropo corrections from correlated data
Scheduling: insert “Geodetic” blocks in schedule
  sched: GEOSEG as scan-based parameter
  other control parameters
  egdelzn.key in examples
AIPS (AIPS memo #110)
  DELZN & CLCOR/opcode=atmo
Numerical weather models & ray-tracing
  ggosatm.hg.tuwien.ac.at/proj-ggosatm.html
  astrogeo.org/spd
Brunthaler, Reid, & Falcke 2005, in Future Directions in High-Resolution Astronomy (VLBA 10th anniv.), p.455: “Atmosphere-corrected phase-referencing”
raw
geo-blocks

## Slide 24: Phs-Ref Limitations: Ionosphere
1 TECU = 1.34/ν[GHz] cycles
1
9
3
0
0
3
3
0
1
1
3
0
USAF PIM model run for solar max
TEC color-map scaling: 30 75 135 180

## Slide 25: Ionosphere Mitigation
Dispersive delay  inverse quadratic dependence τ vs. ν
  Dual-frequency (e.g., 2.3, 8.4 GHz)
  widely-separated sub-bands (Brisken et al. 2002, ApJ, 571, 906)
IGS IONEX maps (gridded vTEC)
  .igscb.jpl.nasa.gov/components/prods.html
  5° long. x 2.5° lat., every 2 hr
  h = 450km || σ ~ 2-8 TECU
  Based on ≥150 GPS stations
  Various analysis centers’ solutions
AIPS: TECOR
  VLBI science memo #23
From raw GPS data:
  Ros et al. 2000, A&A, 356, 375
Incorporation of profile info?
  Ionosondes, GPS/LEO occultations
  igscb.jpl.nasa.gov

## Slide 26: Ionosphere: Climatology
The past few solar cycles: solar 10.7cm flux density
Past peak more akin to a solar “medium” condition
Prediction for current solar cycle: nearing solar “minimum”

## Slide 27: Ionosphere: Equations
τp = (∫μpdl ) /c
μg = d (νμp) /dν
N.B. μp < 1

## Slide 28: Ionosphere: References
Davies, K.E. 1990, Ionospheric Radio
  from a more practical view-point; all frequency ranges
Hargreaves, J.K. 1995, Solar-Terrestrial Environment
  ~senior undergrad science in larger context
Kelly, M.C. 1989, Earth’s Ionosphere
  ~grad science, more detail in transport processes
Schunk, R. & Nagy, A. 2009, Ionospheres
  same as above, plus attention to other planets
Budden, K.G., 1988, Propagation of Radio Waves
  frightening math(s) for people way smarter than I…

## Slide 29: Troposphere vs. Ionosphere
Cross-over frequency below which typical ionospheric delay exceeds typical tropospheric delay (at zenith)
  Troposphere: ~7.8 ns (at sea level, STP)
  Ionosphere: -1.34TEC [TECU] / ν2[GHz] ns
νcross-over ~ √TEC / 5.82 GHz
  can expect to encounter different tropospheric & ionospheric vertical  slant mapping functions
for some representative TECs:
TEC [TECU] | Cross-over ν [GHz]
10 | ~1.3
50 | ~2.9
100 | ~4.1

## Slide 30: Wide-field Mapping: FoV limits
Residual delay, rate  slopes in phase vs. freq, time
  Delay = ∂φ/∂ω i.e., via Fourier transform shift theorem;
  Rate = ∂φ/∂t 1 wrap of φ across band = 1/BW [s] of delay)
Delay (& rate) = function of correlated position:
τ0= -[cosδ0{bxcos(tsid-α0) – bysin(tsid-α0)} + bzsinδ0] / c
As one moves away from correlation center, can make a Taylor-expansion of delay (& rate):
  τ (α,δ) = τ (α0,δ0) + Δα ( ∂τ /∂α ) + Δδ ( ∂τ /∂δ )
 leads to residual delays & rates across the field, increasing away from the phase center.
 leads to de-correlations in coherent averaging over frequency (finite BW) and time (finite integrations).

## Slide 31: Wide-field Mapping: Scalings
To maintain ≤10% reduction in response to point-source:
  Wrobel 1995, in “VLBI & the VLBA” , Ch. 21.7.5
Scaling: BW-smearing: inversely with channel-width
time-smearing: inversely with tint, obs. Frequency
Data size would scale as Nfrq x Nint (e.g.,  area)
  Record for single experiment correlated at JIVE = 5.32 TB
  Expected record for an on-going multi-epoch exp. = 14.71 TB

## Slide 32: WFM: Software Correlation
Software correlators can use almost unlimited Nfrq & tint
  PIs can get a much larger single FoV in a huge data-set
Multiple phase-centers: using the extremely wide FoV correlation “internally”, and steering a delay/rate beam to different positions on the sky to integrate on smaller sub-fields within the “internal” wide field:
  Look at a set of specific sources in the field (in-beam phs-refs)
  Chop the full field up into easier-to-eat chunks
As FoV grows, need looms for primary-beam corrections
  EVN has stations ranging from 20 to 100 m

## Slide 33: Space VLBI: Orbiting Antennas
(Much) longer baselines, no atmosphere in the way
HALCA: Feb’97 — Nov’05
  Orbit: r = 12k—27k km; P = 6.3 hr; i = 31°
RadioAstron: launched 18 July 2011
  Orbit: r = 10-70k km — 310-390k km; P ~ 9.5d; i = 51.6°
  329 MHz, 1.6, 5, 22 GHz
  www.asc.rssi.ru/radioastron
Model/correlation issues:
  Satellite position/velocity; proper vs. coordinate time

## Slide 34: Space VLBI: Solar System Targets
Model variations
  Near field / curved wavefront; may bypass some outer planets
  e.g., Duev et al. 2012, A&A, 541, 43
  Sekido & Fukushima 2006, J. Geodesy, 80, 137
Science applications
  Planetary probes (atmospheres, mass distribution, solar wind)
    Huygens (2005 descent onto Titan), Venus/Mars explorers, MEX fly-by of Phobos, BepiColombo (Mercury)
  Tests of GR (PPN γ, ∂G/∂t, deviations from inverse-square law)
    IAU Symp #261: Relavitivity in Fundamental Astronomy
  Frame ties (ecliptic within ICRS)

## Slide 35: Future
Digital back-ends / wider IFs / faster sampling
  Higher total bit-rates (higher sensitivity)
  More flexible frequency configurations
  More linear phase response across base-band channels
Developments in software correlation
  More special-purpose correlation modes / features
More stations: better sensitivity, u-v coverage
  Additional African VLBI stations for N-S baselines
Continuing maturation of real-time e-VLBI
  Better responsiveness (e.g., automatic overrides)
  Better coordination into multi-λ campaigns

## Slide 36: Concepts for the VLBI Tutorial
Review of VLBI- (EVN-) specific quirks
  |B| so long, no truly point-like primary calibrators
  Each station has independent maser time/ν control; different feeds, IF chains, & back-ends.
Processing steps
  Data inspection
  Amplitude calibration (relying on EVN pipeline…)
  Delay / rate / phase calibration (fringing)
  Bandpass calibration
  Imaging / self-cal
ParselTongue wiki:
  www.jive.eu/jivewiki/doku.php?id=parseltongue:parseltongue

## Slide 37: EVN Archive
Feedback Logfiles
Plots
FITS
Pipeline

## Slide 38: Pipeline Outputs (downloads)
Plots up through (rough) images
Prepared ANTAB file (amplitude calibration input)
a priori Flagging file(s) (by time-range, by channel)
AIPS tables
  CL1 = “unity”, typically 15s sampling
  SN1 = TY  GC; CL2 = CL1  SN1 (& parallactic angles)
  FG1 (sums over all input flagging files)
  SN2 = FG1  CL2  fring; CL3 = CL2  SN2
  BP1 = computed after CL3  FG1
Pipleline-calibrated UVFITS (per source)
Notes: 38

## Slide 39: Data Familiarization
FITLD — to load data
LISTR — scan-based summary of observations
PRTAB, TBOUT, PRTAN
  Looking into contents of “tables”
POSSM, VPLOT, UVPLT
  Plots: vs. frequency, vs. time, u-v based
SNPLT
  Plot solution/calibration tables (various y-axes)
Notes: 39

## Slide 40: Amplitude Calibration (I)
VLBI: no truly point-like primary calibrator
  Structure- and/or time-variability at smallest scales
Stations measure power levels on/off load
  Convertible to Tsys [K] via calibrated loads
Sensitivities, gain curves measured at station
SEFD = Tsys(t) / {DPFU * g(z)}
  √{SEFD1*SEFD2} as basis to convert from unitless correlation coefficients to flux densities [Jy]
EVN Pipeline provides JIVE-processed TY table
Notes: 40

## Slide 41: Amplitude Calibration (II)
UVPLT: plot Amp(|uv|)
  Calibrators with simple structure: smooth drop-off
  e.g., A(ρ)  J1(πaρ) for a uniform disk, diameter=a
Poorly calibrated stations appear discrepant
Self-calibration iterations can help bring things into alignment
Notes: 41

## Slide 42: Delay/Rate Calibration
Each antenna has its own “clock” (H-maser)
Each antenna has its own IF-chains, BBCs
  Differing delays (& rates?) per station/pol/subband
Delay  ∂φ/∂ω (phase-slope across band)
Rate  ∂φ/∂t (phase-slope vs.time)
Point-source = flat φ(ω,t)
  Regular variations: clocks, source-structure, etc.
  Irregular variations: propagation, instrumental noise
  φstr doesn’t necessarily close (not station-based)
Notes: 42

## Slide 43: Fringe-fitting
Over short intervals (SOLINT), estimate delay and rate at each station (wrt reference sta.)
  above = “global fringe-fit” (cf. “baseline fringe-fit”)
“Goldilocks” problem for setting SOLINT:
  too short: low SNR
  too long: > atmospheric coherence time [ = f(ω) ]
After fringing, phases should be flat in the individual subbands, and subbands aligned
BPASS: solve for station bandpass (amp/phase)
  removes phase-curvature across individual subbands
Notes: 43

## Slide 44
VLBI (EVN) obs:
What you may have thought before ERIS: artifacts from the dim mists of a Jungian collective unconcious?
More detailed Monte Carlo simulations reveal an altogether different post-ERIS paradigm: